## Slide 1
Magneto-electric Measurements and Driver Synthesis for Spintronic Equipments using Python
UGP presentation by Nikhil Jain, supervised by Dr. Arnab Bose, IIT Kanpur, Academic Year 2024–25
by Nikhil Jain

## Slide 2
Abstract
Automation Goal
Automate magnetoelectric measurement processes efficiently
Devices Used
PBZ60 Power Supply
B2900 Source Measure Unit
SR830 Lock-in Amplifier
Achievements
Synchronized control and real-time data visualization
Applications
Supports magneto-transport studies for spintronic materials

## Slide 3
Introduction
Motivation
Manual measurements are slow and prone to errors
Challenge
Need scalable and reproducible experimental processes
Solution
Python-based automation for device control and data logging

## Slide 4
Devices, Driver Overview and Setup
PBZ60
Programmable current supply by Kikusui
B2900
Precision Source Measure Unit by Keysight
SR830
Lock-in Amplifier from Stanford Research Systems
Install dependencies (pyvisa, Keysight driver)
Python 3.9, pyvisa, instrument drivers,
GPIB-USB adapter
Organize files (sr830.py, pbz60.py, b2900.py)
Run scripts in main.ipynb (VS Code)
Steps

## Slide 5
PBZ60 + B2900
Measurement System
B2900 Role
Set constant current levels
PBZ60 Role
Sweep current values continuously
Voltage Monitoring
Measure output voltage response
Visualization
Separate plots for forward and backward sweeps

## Slide 6
PBZ60 + SR830 Measurement System
Current Sweep
Control current via PBZ60
Voltage Measurement
SR830 records X and Y voltage channels
Real-Time Plotting
Live data visualization with error bars
GUI Features
Start, Stop, Save, Load operations

## Slide 7
PBZ60 + B2900 + SR830 Nested Measurement
Outer Loop
Sweep B2900 current levels
Inner Loop
Sweep PBZ60 current values
Voltage Measurement
SR830 records complex voltage X and Y channels
Data Visualization
Separate plots per B2900 setting, forward and backward sweeps

## Slide 8
Results, Discussion, and Conclusion
Instrument Performance
No errors, reliable device responses
Data Quality
Real-time plots with standard deviation error bars
Automation Benefits
Improved speed, accuracy, and reproducibility
Python Impact
Robust control and scalable experiments

## Slide 11
Future Prospects
Expansion Plans
Integrate DC and AC magnetic field experiments
using Helmholtz coils
Advanced Techniques
Include Ferromagnetic Resonance and spectral analysis
Software Improvements
Cross-platform device drivers, multi-instrument integration
Automation Focus
Enhance automation for next-gen spintronic research

## Slide 12
Thank you!
Acknowledgements
Dr. Arnab Bose
Nayani Om Swarup (230686)
Qcodes community